TITLE :	CLOCK

PROCEDURE :

- Determine material for the clock and determine the size. (Different shapes may be used.)

- Obtain enough material to make the clock.

- If the wood is rough, surface it to thickness using the planner.

- To surface your wood, measure the thickness of your wood and set the surface planer to 1/16” less than the thickness of your wood.

- Run the wood through the planer and then set the planer to 1/16” less than the thickness the wood is currently at, and continue in this fashion until you have reached the desired thickness.

- Crosscut to length (allow 1” for waste).

- Joint one edge on each board on the jointer.

- Using the table saw, cut strips to thickness. (Usually 1 ½”) Cut as many strips as it takes for the width of the clock.

- Arrange the strips, remembering to alternate the grain, and laminate together with bar clamps, on the glue rack.

- Allow the wood to set up at least two hours.  Remove clamps, clean, and return them to the clamp rack.

- Secure your wood to the bench and scrape off the excess glue with a glue scraper.

- Run both sides of your wood through the surface planer.  Refer to 3a and 3b.

- Joint one edge of your wood on the jointer.

- Cut your wood to the exact size on the table saw.  Remember to keep the jointed edge next to the fence on the table saw.

- Layout the clock face onto your wood by using the clock face template.

- Set up the drill press and drill holes ½” into your wood.  You may use a combination of hole sizes – 1”, ¾”, 5/8”, ½”, 3/8”.

- Use a plug cutter on the drill press and cut plugs to match the holes you drilled in the clock face.

- Glue the plugs into the holes.

- Sand plugs flat with a portable belt sander.

- On the drill press, in the center of your clock, drill a 23/64” hole all the way through your clock.

- Turn the clock over, so the face is down, drill a 3” hole part way through the center of your clock.

- Route the top edges of your clock with the shaper router table.

- Sand your clock with #80-#100-#150 grits sand paper.

- Finish with Danish Oil.

- Wax with a paste wax.