TITLE:  FISH WHACKER

MATERIALS:  2 1\2” x 2 1\2” x 14”  (.6 bd. ft. )

# TOOLS AND EQUIPMENT:      SURFACE PLANER             TABLE SAW

# JOINTER	LATHE

BAND SAW	BELT AND DISK SANDER

RADIAL ARM SAW

PROCEDURES:

- Determine the type of wood that you would like to use, figure the cost and have the instructor sign off your plane sheet.

- Acquire three pieces of wood that are 3\4” to 7\8” thick and 14” long.  Make sure that the face grain is smooth and flat.  If not you will need to run them through the surface planer or sand them on the belt sander.

- Dry clamp the three pieces together and make sure that there aren’t any gaps.  Remove the clamps and apply glue and re-clamp.

- Remove the clamps and return them to the clamp rack.

- Clamp your wood in the bench vise and remove the excess glue with a glue scraper.

- Put a 2”x14” board next to the fence on the radial arm saw.  Put your wood next to the scrap piece of wood and square both ends of stock.  Make sure you use the scrape piece of wood, this will keep your wood from coming in contact with the blade before you turn it on.

- Your wood should be square, if it isn’t run it through the surface planer.

- Cut diagonal lines from corner to corner on both ends with the band saw.  Use the large band saw for this operation.

- Set the jointer fence to a 45-degree angle.  Run each edge through the jointer so that you have a 1\2” bevel.  This will take multiple passes through the jointer.

- Set up your stock on the lathe between centers.  Use a gouge of a diamond point tool and turn the stock completely round.  Keep the diameter as large as you can.

- The next step is to shape the fish whacker.  The best way is to have a scale drawing or it can be free handed.  Whichever way you decide on use the round nose tool for shaping.  Leave 1\2” waste on each end so that the diagonal lines that you cut on the band saw will not show.  Measure 1\2” from each end and cut a grove 3\4” deep into both ends with the parting tool.

- Once you have the shape that you want remove the tool rest and sand your project with #80-#100-#150 grits sandpaper.

- Ask the instructor for assistance for decreasing the ends with the parting tool.

- Sand off the ends with the disk sander.

- Finish sand the ends with #100-#150 grits sandpaper.

- Apply Danish Oil.  Refer to the oiling instructions.

- Apply wax.  Refer to the waxing instructions.