TITLE:  WOOD BOX	MATERIALS:

2 sides 1\2" x 3" x 10"

2 ends  1\2" x 3”x 5”

2 top and bottom 1\2" x 6" x 10 1\2"

MATERIAL AMOUNT: 1.5 bd. ft.

# TOOLS:	Radial arm saw 	Belt and disk sander

Table saw	Vibrating Sander

Band Saw	Router

Jointer

PROCEDURES:

1. 	Secure material from the instructor.

2. 	Surface your material to 1\2" thickness.

3. 	Joint one edge of your material on the jointer

4. 	Rip your wood to 3" in width on the table saw.

5. 	Cut two ends to 5" and two sides to 10" in length on the radial arm saw.

6. 	On the table saw cut a rabbit joint on both ends of the 10" sidepieces.

7. 	Glue the four pieces together using the metal band clamps.  You'll need to use two of these clamps, one on the bottom and one on the top.

8. 	Sand the top and bottom edges on the 14" disk sander.

9. 	Find the wood for your top and bottom.  The board should be close to 6" x 21".

10.	Surface plane your wood to 1\2" thickness.

11.	Using the radial arm saw cut your wood in half.

12.	Glue the top and bottom pieces to your box with three parallel clamps.

13.	Cut off the excess of your top and bottom on the band saw.

14.	Sand all sides on the belt sander.

15.	Route the edges on the shaper router table with a 3\8" rounding over bit.

16.	Sand the box with a vibrating sander using 80-100-150 grits sandpaper.

17.	The box needs to be cut on the table saw so that you have a top and bottom.  Set the table saw up so the blade is a little over 1\2" in height and the fence is set at 1 3\8" from the blade.  Have the instructor check your set up before you cut your lid.

18.	Sand your two edges on the 14" disk sander.

19.	Route the two edges on the shaper router table with a 1\4" rounding over bit.

20.	Sand these two edges by hand with 150 grit sandpaper.

21.	Oil your box with Danish Oil.

22.	Put on hinges.

23.	Talk to the instructor about lining your box with felt of velvet.